## Slide 1
OWEN EDWARDS
TRICS CONSORTIUM
REGIONAL TRIP RATES
VARIATION IN TRICS

## Slide 2
OWEN EDWARDS
TRICS CONSORTIUM
Often brought up by users requesting guidance on trip rates survey samples
Basic regional variation research
was carried out in the past

## Slide 3
OWEN EDWARDS
TRICS CONSORTIUM
Previous work suggested less regional variation than generally assumed
TRICS would like to confirm or confront previous findings

## Slide 4
OWEN EDWARDS
TRICS CONSORTIUM
New research split into two phases leading to a final technical note
Initial phase to look into trip rates across a variety of popular land uses

## Slide 5
OWEN EDWARDS
TRICS CONSORTIUM
CURRENT GOOD
PRACTICE GUIDANCE

## Slide 6
OWEN EDWARDS
TRICS CONSORTIUM
Regional selection is not as important a factor as location type and other important factors
The importance of compatibility in terms of local population, vehicle ownership, location type, etc, cannot be stressed enough

## Slide 7
OWEN EDWARDS
TRICS CONSORTIUM
No obvious reason why some data from Glasgow cannot apply to some data from Greater Manchester
Similarly, some site scenarios in parts of London may be compatible with sites in other large cities

## Slide 8
OWEN EDWARDS
TRICS CONSORTIUM
It is in the areas of site and development data where true compatibility should be sought, rather than just through the exclusion of regions, which could unnecessarily remove many compatible sites from a user’s selected set

## Slide 9
OWEN EDWARDS
TRICS CONSORTIUM
TRICS
REGIONS

## Slide 10
OWEN EDWARDS
TRICS CONSORTIUM
1 Greater London
2 South East
3 South West
4 East Anglia
5 East Midlands
6 West Midlands
7 Yorkshire & North Lincolnshire
8 North West
9 North
10 Wales
11 Scotland
12 Connaught
13 Munster
14 Leinster
15 Greater Dublin
16 Ulster Ireland
17 Ulster Northern Ireland

## Slide 11
OWEN EDWARDS
TRICS CONSORTIUM
GROUPED
REGIONS

## Slide 12
OWEN EDWARDS
TRICS CONSORTIUM
Number of surveys in each TRICS region varies massively
Where possible, similar regions are grouped together to see how these results compare to the rest

## Slide 13
OWEN EDWARDS
TRICS CONSORTIUM
Certain regions were grouped together for calculating trip rates
5 East Midlands, 6 West Midlands
----------------
7 Yorkshire & North Lincolnshire, 8 North West, 9 North
----------------
12 Connaught, 13 Munster, 14 Leinster, 15 Greater Dublin, 16 Ulster Ireland, 17 Ulster Northern Ireland

## Slide 14
OWEN EDWARDS
TRICS CONSORTIUM
Using grouped regions results in six major regions to focus on
1 Greater London
2 South East
3 South West
5-6 Unified Midlands
7-9 Unified North
12-17 Unified Ireland

## Slide 15
OWEN EDWARDS
TRICS CONSORTIUM
LAND
USES

## Slide 16
OWEN EDWARDS
TRICS CONSORTIUM
Most popular land uses selected
01/A Food Superstore
02/A Office
03/A Houses Privately Owned

## Slide 17
OWEN EDWARDS
TRICS CONSORTIUM
01/A Food Superstore split into Friday only and Saturday only surveys
02/A Office and 03/A Houses Privately Owned will use only weekday surveys

## Slide 18
OWEN EDWARDS
TRICS CONSORTIUM
SELECTION
PARAMTERS

## Slide 19
OWEN EDWARDS
TRICS CONSORTIUM
As many surveys wanted to keep the samples as large as possible
Vehicles Only surveys
Looking at surveys from the past 20 years, minimum date set to 01/01/1999
All location types included

## Slide 20
OWEN EDWARDS
TRICS CONSORTIUM
01/A FOOD SUPERSTORE FRIDAY RESULTS

## Slide 21
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (59) | Peak Totals (12.273)
3 South West | 9 | 14.629
12-17 Unified Ireland | 9 | 14.056
2 South East | 8 | 12.325
7-9 Unified North | 7 | 12.266
5-6 Unified Midlands | 11 | 11.736
1 Greater London | 3 | 7.299
01/A FOOD SUPERSTORE FRIDAY
Results per 100m²

## Slide 22
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (59) | Peak Totals (12.273)
17 Ulster Northern Ireland | 6 | 18.978
3 South West | 9 | 14.629
12-17 Unified Ireland | 9 | 14.056
10 Wales | 4 | 13.875
9 North | 4 | 13.354
… | … | …
5 East Midlands | 8 | 12.098
5-6 Unified Midlands | 11 | 11.736
6 West Midlands | 3 | 10.411
11 Scotland | 4 | 9.806
1 Greater London | 3 | 7.299
01/A FOOD SUPERSTORE FRIDAY
Results per 100m²

## Slide 23
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (59) | Trips Totals (146.938)
3 South West | 9 | 187.741
12-17 Unified Ireland | 9 | 157.722
2 South East | 8 | 154.470
7-9 Unified North | 7 | 139.858
5-6 Unified Midlands | 11 | 134.661
1 Greater London | 3 | 77.657
01/A FOOD SUPERSTORE FRIDAY
Results per 100m²

## Slide 24
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (59) | Trips Totals (146.938)
17 Ulster Northern Ireland | 6 | 201.851
3 South West | 9 | 187.741
12-17 Unified Ireland | 9 | 157.722
2 South East | 8 | 154.470
9 North | 4 | 147.112
… | … | …
10 Wales | 4 | 139.479
5-6 Unified Midlands | 11 | 134.661
6 West Midlands | 3 | 106.131
11 Scotland | 4 | 90.652
1 Greater London | 3 | 77.657
01/A FOOD SUPERSTORE FRIDAY
Results per 100m²

## Slide 25
OWEN EDWARDS
TRICS CONSORTIUM
This data sample shows South West, Unified Ireland and North with slightly higher vehicle trip rates
This data sample shows Greater London, Scotland and Unified Midlands with slightly lower vehicle trip rates

## Slide 26
OWEN EDWARDS
TRICS CONSORTIUM
01/A FOOD SUPERSTORE SATURDAY RESULTS

## Slide 27
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (79) | Peak Totals (12.617)
3 South West | 9 | 14.486
7-9 Unified North | 16 | 13.647
2 South East | 15 | 12.886
5-6 Unified Midlands | 10 | 12.878
12-17 Unified Ireland | 5 | 10.730
1 Greater London | 7 | 8.788
01/A FOOD SUPERSTORE SATURDAY
Results per 100m²

## Slide 28
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (79) | Peak Totals (12.617)
4 East Anglia | 3 | 18.391
10 Wales | 7 | 14.804
7 Yorkshire & North Lincolnshire | 6 | 14.633
3 South West | 9 | 14.486
8 North West | 4 | 14.304
… | … | …
5-6 Unified Midlands | 10 | 12.878
17 Ulster Northern Ireland | 4 | 11.525
12-17 Unified Ireland | 5 | 10.730
11 Scotland | 7 | 9.755
1 Greater London | 7 | 8.788
01/A FOOD SUPERSTORE SATURDAY
Results per 100m²

## Slide 29
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (79) | Trips Totals (142.324)
3 South West | 9 | 182.402
7-9 Unified North | 16 | 145.470
5-6 Unified Midlands | 10 | 135.579
2 South East | 15 | 134.599
12-17 Unified Ireland | 5 | 105.874
1 Greater London | 7 | 95.211
01/A FOOD SUPERSTORE SATURDAY
Results per 100m²

## Slide 30
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (79) | Trips Totals (142.324)
4 East Anglia | 3 | 190.215
3 South West | 9 | 182.402
7 Yorkshire & North Lincolnshire | 6 | 151.846
10 Wales | 7 | 148.896
7-9 Unified North | 16 | 145.470
… | … | …
2 South East | 15 | 134.599
17 Ulster Northern Ireland | 4 | 110.062
12-17 Unified Ireland | 5 | 105.874
11 Scotland | 7 | 98.821
1 Greater London | 7 | 95.211
01/A FOOD SUPERSTORE SATURDAY
Results per 100m²

## Slide 31
OWEN EDWARDS
TRICS CONSORTIUM
In these two data samples, only Wales and South West remain in the top five regions from Friday to Saturday peak totals
In these two data samples, only Greater London and Scotland remain in the bottom five regions from Friday to Saturday trips totals

## Slide 32
OWEN EDWARDS
TRICS CONSORTIUM
02/A OFFICE
WEEKDAY RESULTS

## Slide 33
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (134) | Peak Totals (0.723)
7-9 Unified North | 26 | 1.073
3 South West | 6 | 1.045
2 South East | 30 | 0.826
12-17 Unified Ireland | 17 | 0.550
5-6 Unified Midlands | 10 | 0.522
1 Greater London | 20 | 0.326
02/A OFFICE WEEKDAY
Results per 100m²

## Slide 34
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (134) | Peak Totals (0.723)
16 Ulster Ireland | 4 | 1.924
7 Yorkshire & North Lincolnshire | 4 | 1.876
10 Wales | 6 | 1.537
4 East Anglia | 10 | 1.118
9 North | 14 | 1.073
… | … | …
12-17 Unified Ireland | 17 | 0.550
5-6 Unified Midlands | 10 | 0.522
6 West Midlands | 7 | 0.424
1 Greater London | 20 | 0.326
15 Greater Dublin | 5 | 0.312
02/A OFFICE WEEKDAY
Results per 100m²

## Slide 35
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (134) | Trips Totals (10.685)
7-9 Unified North | 26 | 15.699
3 South West | 6 | 15.016
2 South East | 30 | 10.342
12-17 Unified Ireland | 17 | 8.244
5-6 Unified Midlands | 10 | 7.095
1 Greater London | 20 | 5.136
02/A OFFICE WEEKDAY
Results per 100m²

## Slide 36
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (134) | Trips Totals (10.685)
16 Ulster Ireland | 4 | 23.468
7 Yorkshire & North Lincolnshire | 4 | 20.019
9 North | 14 | 16.905
5 East Midlands | 3 | 16.473
10 Wales | 6 | 15.949
… | … | …
12-17 Unified Ireland | 17 | 8.244
5-6 Unified Midlands | 10 | 7.095
1 Greater London | 20 | 5.136
6 West Midlands | 7 | 4.482
15 Greater Dublin | 5 | 3.609
02/A OFFICE WEEKDAY
Results per 100m²

## Slide 37
OWEN EDWARDS
TRICS CONSORTIUM
In this data sample East Midlands produces slightly higher trip rates but West Midlands slightly lower
In this data sample Unified Ireland produces slightly lower vehicle trip rates despite Ulster Ireland producing slightly higher

## Slide 38
OWEN EDWARDS
TRICS CONSORTIUM
03/A HOUSES PRIVATELY OWNED WEEKDAY RESULTS

## Slide 39
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (202) | Peak Totals (0.593)
12-17 Unified Ireland | 54 | 0.700
5-6 Unified Midlands | 28 | 0.618
3 South West | 11 | 0.573
1 Greater London | 10 | 0.565
2 South East | 27 | 0.534
7-9 Unified North | 37 | 0.516
03/A HOUSES PRIVATELY OWNED
Results per dwelling

## Slide 40
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (202) | Peak Totals (0.593)
14 Leinster | 6 | 0.840
17 Ulster Northern Ireland | 17 | 0.806
12 Connaught | 15 | 0.705
12-17 Unified Ireland | 54 | 0.700
5 East Midlands | 7 | 0.692
… | … | …
15 Greater Dublin | 7 | 0.564
2 South East | 27 | 0.534
9 North | 9 | 0.519
7-9 Unified North | 37 | 0.516
7 Yorkshire & North Lincolnshire | 13 | 0.456
03/A HOUSES PRIVATELY OWNED
Results per dwelling

## Slide 41
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (202) | Trips Totals (6.968)
12-17 Unified Ireland | 54 | 8.315
1 Greater London | 10 | 6.449
2 South East | 27 | 6.120
5-6 Unified Midlands | 28 | 5.075
3 South West | 11 | 4.921
7-9 Unified North | 37 | 4.589
03/A HOUSES PRIVATELY OWNED
Results per dwelling

## Slide 42
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys (202) | Trips Totals (6.968)
17 Ulster Northern Ireland | 17 | 8.776
12-17 Unified Ireland | 54 | 8.315
14 Leinster | 6 | 7.642
11 Scotland | 14 | 7.225
1 Greater London | 10 | 6.449
… | … | …
10 Wales | 8 | 4.892
15 Greater Dublin | 7 | 4.699
9 North | 9 | 0.519
7-9 Unified North | 37 | 4.589
7 Yorkshire & North Lincolnshire | 13 | 3.904
03/A HOUSES PRIVATELY OWNED
Results per dwelling

## Slide 43
OWEN EDWARDS
TRICS CONSORTIUM
Greater London produces just below average trips totals but still slightly higher than other regions in this data sample
Yorkshire & North Lincolnshire and North produce slightly lower peak and trips totals in this data sample

## Slide 44
OWEN EDWARDS
TRICS CONSORTIUM
CROSS LAND
USE RESULTS

## Slide 45
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | 01/AF | 01/AS | 02/AW | 03/AW
1 Greater London | 6th | 6th | 6th | 4th
2 South East | 3rd | 3rd | 3rd | 5th
3 South West | 1st | 1st | 2nd | 3rd
5-6 Unified Midlands | 5th | 4th | 5th | 2nd
7-9 Unified North | 4th | 2nd | 1st | 6th
12-17 Unified Ireland | 2nd | 5th | 4th | 1st
CROSS LAND USE RANKINGS
Based on Peak Totals

## Slide 46
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | 01/AF | 01/AS | 02/AW | 03/AW
1 Greater London | 6th | 6th | 6th | 2nd
2 South East | 3rd | 4th | 3rd | 3rd
3 South West | 1st | 1st | 2nd | 5th
5-6 Unified Midlands | 5th | 3rd | 5th | 4th
7-9 Unified North | 4th | 2nd | 1st | 6th
12-17 Unified Ireland | 2nd | 5th | 4th | 1st
CROSS LAND USE RANKINGS
Based on Trips Totals

## Slide 47
OWEN EDWARDS
TRICS CONSORTIUM
Different land uses give significantly different results
For these data samples regions can be top of a ranking for one land use but bottom of a ranking for another

## Slide 48
OWEN EDWARDS
TRICS CONSORTIUM
Rather than regional variance, other important factors such as location type, public transport levels, local population, car ownership can be much more significant
All these are adjustable parameters within the TRICS software

## Slide 49
OWEN EDWARDS
TRICS CONSORTIUM
Using the four data samples, it is possible to view each major region’s variance ranges from the average of all surveys
The two tables are based on total peak figures and total trips figures

## Slide 50
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys | High | Low | Average
1 Greater London | 40 | -4.7 | -54.9 | -32.6
2 South East | 80 | +14.2 | -9.9 | +1.7
3 South West | 35 | +44.5 | -3.4 | +18.8
5-6 Unified Midlands | 59 | +4.2 | -27.8 | -6.5
7-9 Unified North | 86 | +48.4 | -13.0 | +10.9
12-17 Unified Ireland | 85 | +18.0 | -23.9 | -1.6
TRIP GENERATION RANGES SUMMARY
Total Peak figures

## Slide 51
OWEN EDWARDS
TRICS CONSORTIUM
TRICS Regions | Surveys | High | Low | Average
1 Greater London | 40 | -7.4 | -51.9 | -34.9
2 South East | 80 | +5.1 | -12.2 | -3.9
3 South West | 35 | +40.5 | -29.4 | +16.8
5-6 Unified Midlands | 59 | -4.7 | -33.6 | -18.5
7-9 Unified North | 86 | +46.9 | -34.1 | +2.5
12-17 Unified Ireland | 85 | +19.3 | -25.6 | -5.4
TRIP GENERATION RANGES SUMMARY
Total Trips figures

## Slide 52
OWEN EDWARDS
TRICS CONSORTIUM
REGIONAL TRIP RATES VARIATION INITIAL FINDINGS

## Slide 53
OWEN EDWARDS
TRICS CONSORTIUM
Initial findings indicate there is no evidence for fundamental direct regional influences on trip rates
This suggests current Good Practice Guidance remains valid and further research into location type variation will give greater clarity

## Slide 54
OWEN EDWARDS
TRICS CONSORTIUM
Due to a limited number of surveys in each region across all four data samples, it is important to note these figures cannot indicate specific trends outside of the standard trip rate variation regularly observed when using TRICS

## Slide 55
OWEN EDWARDS
TRICS CONSORTIUM
Many regions featured both slightly higher or lower trip rates across the four different land uses
This indicates a number of factors can influence trip rates variation and does not provide any evidence of fundamental regional influence

## Slide 56
OWEN EDWARDS
TRICS CONSORTIUM
TRIP RATES
INFLUENCES

## Slide 57
OWEN EDWARDS
TRICS CONSORTIUM
Instead of deselecting a region, ask why you have made a regional presumption about its trip rates
TRICS includes parameters for location type, local populations, public transport pass-bys, car ownership levels, etc

## Slide 58
OWEN EDWARDS
TRICS CONSORTIUM
FURTHER
RESEARCH

## Slide 59
OWEN EDWARDS
TRICS CONSORTIUM
Following on from this initial work, it is intended to look similarly at the influence of location types
The findings of these two works will be combined to create a new Regional and Location Technical Note